## Slide 1
FF
FOCUS FINDER
Real-time campus noise monitoring for students
TEAM
Elias Aschenbrenner
Jay Nibhanupudy
Bernard Krasuski
Shiner Supre
COURSE
CIS4930 · Full Stack IoT Development
Final Project Presentation
Herbert Wertheim College of Engineering
University of Florida · Spring 2026

## Slide 2
INTRODUCTION
Quiet study space shouldn't be a scavenger hunt
THE PROBLEM
Moderate ambient noise
significantly impairs
cognitive tasks, concentration, and problem-solving
STUDENT BEHAVIOR
Building-to-building hunting
Students waste time between classes searching for a spot that's actually quiet — often showing up to a library floor only to turn around.
WHY EXISTING TOOLS FALL SHORT
SoundPrint & similar apps
Manual, subjective ratings — no sensors, no live data
City-scale noise maps
Great for urban planning — wrong scale for a campus library
Library camera occupancy
Counts bodies, not decibels; people can be silent or loud
OUR FUNCTIONAL REQUIREMENTS
Measure noise objectively · Deliver it live · Show it where students already look — their phone
A Level-4 distributed IoT system: multiple sensor nodes sample dB locally, push through a gateway to the cloud, and render a mobile-friendly campus heat map with live updates and historical trends.
Introduction & Motivation
Focus Finder · 2 / 13

## Slide 3
DESIGN · SYSTEM OVERVIEW
Level-4 IoT: sensors → gateway → cloud → phone
SENSOR NODES
ESP32 + sensors
INMP441 MEMS mic (I²S)
MPU-6050 IMU (I²C)
HC-SR04 ultrasonic
Samples every 3 s
LOCAL LINK
ESP-NOW
Peer-to-peer, no router
~250 B payload
Works if WiFi drops
Gateway aggregates
CLOUD
Firebase Realtime DB
Gateway POSTs via HTTPS
/readings/{node_id}
Cloud Functions validate
TLS + API key
CLIENT
React PWA
Firebase SDK onValue()
Live heat map
Predictions + history
Mobile-first UI
IMPLEMENTATION CHANGE FROM PROPOSAL
Sensor nodes no longer POST directly to Firebase. They now use ESP-NOW to a gateway ESP32, which handles the HTTPS leg. This satisfies our multi-MCU requirement, reduces per-node battery draw, and keeps Wi-Fi credentials off every sensor.
2
Sensor nodes (demo)
1
Gateway MCU
3 s
Sample interval
3
Sensor types per node
< 30 s
End-to-end latency
Design · Architecture
Focus Finder · 3 / 13

## Slide 4
DESIGN · HARDWARE
Sensors and MCU features we leverage
SENSORS
INMP441 MEMS Microphone
I²S
Captures 16 kHz / 32-bit PCM samples. We compute a rolling RMS on-chip and only ship the derived dB value — raw audio never leaves the device.
MPU-6050 IMU (accel + gyro)
I²C
Continuously polled for tilt/shock. If readings cross a threshold the node flags 'tamper' — critical for public-space deployment.
HC-SR04 Ultrasonic
GPIO (pulse)
Added during development for presence sensing — distinguishes 'room is empty and quiet' from 'room is occupied and quiet'.
ESP32-WROOM-32 · FEATURES USED
Dual-core Xtensa LX6
RMS DSP on one core, radio + housekeeping on the other
Hardware I²S peripheral
Clocks the INMP441 without CPU-bit-banging
ESP-NOW radio mode
2.4 GHz peer protocol — no AP or IP stack needed
Station-mode Wi-Fi + TLS
Used only on the gateway for the HTTPS hop to Firebase
Deep-sleep capable
Enables the battery strategy in the sustainability slide
WIRING AT A GLANCE
INMP441 → SCK 26, WS 25, SD 23 (I²S0)
MPU-6050 → SDA 21, SCL 22 (I²C, 0x68)
HC-SR04 → TRIG 18, ECHO 19
Power → USB-C, 3V3 rail, common GND
Deployed in 3D-printed, smoke-detector-sized shells mounted on walls/ceilings
Design · Hardware
Focus Finder · 4 / 13

## Slide 5
DESIGN · COMMUNICATION
Two hops: ESP-NOW locally, HTTPS to the cloud
HOP 1 · Sensor → Gateway
ESP-NOW
2.4 GHz ESP-proprietary peer protocol
STRENGTHS
No access point needed — works if campus Wi-Fi drops
~250-byte packed struct, microsecond-class latency
No TCP/IP stack on the sensor — smaller firmware footprint
Sensor never holds Wi-Fi credentials — smaller attack surface
TRADE-OFFS
No encryption by default at our range — acceptable because packets carry only a dB value
Best-effort delivery, so we accept occasional drops and rely on the 3-s cadence
HOP 2 · Gateway → Cloud
HTTPS / REST (JSON)
TLS 1.2 over Wi-Fi to Firebase Realtime DB
STRENGTHS
Encrypted in transit — mitigates MITM on open campus networks
Standard REST surface: cloud functions validate API key
JSON is self-describing — easy to evolve the schema
Firebase handles reconnect, caching, and fan-out
TRADE-OFFS
TLS handshake is expensive — centralizing it on one gateway is the whole reason we split hops
Single gateway is a failure point — future: secondary gateway on a different SSID
Design · Communication
Focus Finder · 5 / 13

## Slide 6
DESIGN · CLOUD
Firebase Realtime DB + Cloud Functions
WHY NoSQL FOR THIS DATA
Readings are time-series documents keyed by node — no joins, no foreign keys, just append and fan out.
TRADITIONAL SQL
FIREBASE REALTIME DB
Schema ceremony ✗
Free to add battery_pct, tamper, distance_cm as sensors evolved
Join-heavy reporting ✗
One flat path per node; chart code just iterates
Row-level locking ✗
Last-write-wins push is fine — readings are immutable once stored
Polling ✗
onValue() listeners push updates to the client in real time
SCALING STORY
3 nodes × 1 reading / 3 s = 86,400 writes / day
Well within Firebase's free Spark tier.
A full campus (100 nodes) = 2.88M writes / day — stays affordable with a 1-min downsample function writing only aggregates.
STORED RECORD
/readings/{node_id}.push({
noise_db: 58,
accel_x/y/z: 0.03, -0.01, 0.99,
gyro_x/y/z: 0.8, 1.2, -0.1,
distance_cm: 142.3,
battery_pct: 87,
timestamp: 1732818600123
})
Design · Cloud
Focus Finder · 6 / 13

## Slide 7
DESIGN · CLIENT
React PWA — architecture and accessibility
APPLICATION ARCHITECTURE
React 18 + Vite
Component tree, hot-reloaded in dev
Firebase Web SDK
onValue() subscriptions push live updates into useState
Recharts + SVG
Declarative charts; floor plan hand-rolled in SVG for exact zoning
WHY CLIENT-HEAVY SPA
No server to maintain beyond Firebase
Each phone subscribes directly; live updates without polling
Ships as a static bundle → trivial caching / offline fallback
TRADE-OFF
Business logic lives in the browser — if we needed multi-writer consistency or complex permissions, we'd move compute to Cloud Functions.
ACCESSIBLE BY DESIGN
Noise level is information students act on in seconds — glance-first UX was a hard requirement.
Colour + text always paired
Quiet/Moderate/Loud bands are labelled, not colour-only — works for colour-vision deficiency
WCAG-AA contrast on every dB
Navy (#1A3A6B) on white, orange accents tested with axe
No login required
Dropping a barrier for students between classes
Touch targets ≥ 44 px
Floor-plan zones and nav bar items sized for thumbs, not cursors
Semantic HTML + ARIA labels
Nav, headings, and SVG titles readable by screen readers
Reduced-motion respected
The live-dot pulse honours prefers-reduced-motion (future polish)
Design · Client & Accessibility
Focus Finder · 7 / 13

## Slide 8
DESIGN · SUSTAINABILITY
Power budget and lifecycle choices
PER-NODE POWER BUDGET (5 V USB-C)
Component
Active draw
Duty
Avg draw
ESP32-WROOM-32
~160 mA
60%
~96 mA
INMP441 microphone
1.4 mA
100%
1.4 mA
MPU-6050 IMU
3.9 mA
100%
3.9 mA
HC-SR04 ultrasonic
15 mA
3%
~0.5 mA
Sensor node total
—
—
≈ 102 mA
Gateway total
—
—
≈ 180 mA
Measured on the bench — numbers include brownout margin. Idle-mode optimisation is the next step (see right).
SUSTAINABLE DEVELOPMENT
ENERGY
Gateway aggregates; sensor nodes do the cheap work. Future deep-sleep cycle targets <20 mA average.
LIFECYCLE
Off-the-shelf modules, pluggable sensors. A dead IMU swaps in a minute without reflashing.
3D-PRINTED SHELL
PLA filament, ~150 g per enclosure. Recyclable through the college makerspace programme.
MAINTAINABILITY
OTA firmware path is planned; remote tamper-reset already implemented via the database.
Design · Sustainability
Focus Finder · 8 / 13

## Slide 9
DESIGN · SECURITY
Attack surface and what we hardened
THREAT MODEL
Public hardware in a library, open campus Wi-Fi, and a microphone sensor — the risks are privacy (audio), data injection (spoofed nodes), and physical tamper.
ATTACK VECTOR
Audio exfiltration
MITIGATION
All DSP on-device. Only a dB integer leaves the node — raw audio is never buffered long enough to transmit.
ATTACK VECTOR
Man-in-the-middle
MITIGATION
Gateway ⇄ Firebase runs over TLS 1.2. Cloud Function rejects any POST missing a matching API key.
ATTACK VECTOR
Rogue sensor injection
MITIGATION
Gateway only unpacks packets from known ESP-NOW peers. Cloud writes validate the node_id allow-list.
ATTACK VECTOR
Physical tamper
MITIGATION
MPU-6050 flags shock/tilt. Gateway writes tamper:true; the UI shows the zone as 'Unreliable' until an admin resets it.
Design · Security
Focus Finder · 9 / 13

## Slide 10
AI / ML
We didn't use ML — here's where it would go
TODAY — STATISTICAL BASELINE
"Usually busy"-style predictions
Prediction today is a deterministic lookup: per-hour time-of-day multiplier × weekend factor × per-zone base level.
predictNoise(zone, hoursFromNow) {
hour = (now + hoursFromNow) % 24
weekendFactor = isWeekend ? 0.73 : 1.0
return zone.baseNoise
* TIME_MULTIPLIERS[hour]
* weekendFactor
}
Transparent, runs client-side, zero inference cost — but misses one-off events (exams, gamedays).
FUTURE — WHERE ML WOULD HELP
Short-horizon forecasting
A lightweight Seasonal-ARIMA (or Prophet) trained per zone on 2–4 weeks of 5-min averages. Target the 30–120 minute window — when will it quiet down?
Anomaly detection
Unsupervised IsolationForest on (dB, accel, distance) to flag events the static threshold misses — e.g. a spike that isn't tamper but isn't normal chatter either.
Data strategy
We'd backfill from the Firebase readings we're already collecting. Labels for 'actually quiet / not quiet' come from an in-app thumbs-up/down.
Evaluation
MAE on predicted dB (target < 4 dB), and classification F1 on the 3-way Quiet/Moderate/Loud label (target > 0.85, per zone).
AI / ML
Focus Finder · 10 / 13

## Slide 11
TASK MANAGEMENT
Timeline and collaboration
UPDATED TIMELINE · JAN – APR
Jan
Feb
Mar
Apr
Literature review + proposal
Component procurement
Firmware — sensor sampling
ESP-NOW gateway firmware
Firebase + cloud functions
React frontend + heat map
Midpoint demo
3D-printed enclosures
Integration + tamper path
Final testing + presentation
Planning
Build
Milestone
Test
GITHUB INSIGHTS · SINCE MIDPOINT
4
active contributors
2
codebases · firmware + web
All
members touched ≥ 2 areas
0
merges blocked on a single person
Task Management
Focus Finder · 11 / 13

## Slide 12
LIVE DEMO
Two ESP32 sensor nodes · one gateway · live web dashboard
LIVE READING
Decibel value streams in under 30 seconds
We'll play a calibrated noise clip. Watch the floor-plan zone change colour Green → Yellow → Red in real time.
TAMPER ALERT
Physical movement flips the zone to 'Unreliable'
One of us will pick up a node. The IMU threshold fires, the gateway writes tamper:true, the UI drops that zone from the quiet-spots list.
PREDICTIONS
The +1 hr / +2 hr toggle re-colours every zone
Showing that the historical baseline is wired through to the same heat-map component — not a separate screen.
Demonstration of Functionality
Focus Finder · 12 / 13

## Slide 13
REFLECTION
What we'd build next
FUTURE CI/CD TESTING PIPELINE
COMMIT
GitHub push
BUILD
PlatformIO + Vite
UNIT
Jest · dB math, predict fn
INTEGRATE
Firebase emulator + replay
DEPLOY
Prod or staging
PERFORMANCE METRICS WE'D GATE ON
≤ 3 dB
sensor accuracy vs reference meter
≤ 30 s
sound-event → dashboard latency
< 5 %
tamper false-positive rate
≥ 95 %
node uptime
MAE
on predicted dB (per zone)
NEXT ENERGY WIN
Deep-sleep between samples
Sensor nodes sleep ~2.7 s out of every 3 — ESP32 RTC wakes the I²S peripheral, samples, sleeps again. Projected average: ~10 mA (from ~102 mA). Combined with a 2000 mAh LiPo and a small solar trickle-charger, we could untether nodes from wall power and get useful battery life without grid access.
Reflection
Focus Finder · 13 / 13